## Slide 1: EE 421 / CS 425 Digital System Design Fall 2026 Lecture 8
Shahid Masud
State Machines
Vending Machine Example

## Slide 2: Topics
State Diagrams
Introduction to State Machines
Moore State Machine and Mealy State Machine
State Tables Description of State Machines
Design Example of a State Machine (Vending Machine)
Sequential State Machine Circuit Design
One Hot Encoding and ASMD
ANNOUNCEMENT
QUIZ 2
Next Lecture

## Slide 3: Practice Questions from Past Papers
Check folders:
SSE → EE 421
and
CS → CMPE 424
and
CS → CS 424

## Slide 4: State Diagram of D Flipflop
Input (D) | Next State (Q)
0 | 0 (D)
1 | 1 (D)
0
1
1/1
0/0
0/0
DFF
1/1
Input to System
Output of System
Internal
States
Internal
States

## Slide 5: State Diagram of T Flipflop
Input (T) | Next State (Q)
0 | Q
1 | Q’
0
1
0
1
0
TFF
1

## Slide 6: Linking State Table with State Diagram
Q (t) | Q (t+1) |  | Z (Output) | 
 | Input X=0 | Input X=1 | Input X=0 | Input X=1
A | A | B | 0 | 0
B | C | B | 1 | 0
C | A | D | 0 | 0
D | C | C | 0 | 0
Complete State Description Including Inputs, Present State, Outputs and Next State
A
X/0
0/0
B
C
D
1/0
0/1
1/0
0/0
1/0

## Slide 7: Types of State Machines
Mealy Machine
  Output depends upon Internal State plus External Inputs
  Output can change at any time and not necessarily after a Clocked event
Moore Machine
  Output depends upon External Inputs and Current Internal State
  Output is Synchronized with the Change in Internal States

## Slide 8: Mealy State Machine Block Diagram
Next State Logic
State Registers
Output Logic
Inputs
X
Outputs
Y
Clk

## Slide 9: State Machine Block Diagrams - Comparison
Next State Logic
State Registers
Output Logic
Inputs
X
Outputs
Y
Next State Logic
State Registers
Output Logic
Inputs
X
Outputs
Y
Moore
Mealy
Side by side
Clk
Clk

## Slide 10: State Machine Based Synchronous Design
Understand the Problem – desired sequence based on inputs and present state
Develop abstract representation of FSM – A state diagram or a state table that shows all possible states and transitions
Perform state minimization – to achieve efficient implementation
Perform state assignment
Choose appropriate flipflop for storage elements (eg. D flipflops)
Use K-maps to determine characteristic equations for Next State
After K-maps based minimization; draw complete logic circuit using combinational and sequential elements

## Slide 11: Example of a State Machine Based Design – Coke (Next Cola ) Vending Machine
Machine dispenses a can of coke for Rs. 15/-
You can provide coins of either Rs. 5/- or Rs. 10/-
The Machine does not provide any change back
The Machine is ‘Reset’ after the can has been dispensed

## Slide 12: Block Diagram of Vending Machine Example
Coin
Sensor
Input Logic
Vending
Machine
State Machine
Output
Logic
Reset
Coins
R5, R10
State Machine
Input
Next State
Dispense
Question: Which type is this? Moore or Mealy??
Is Input Directly Connected to Output Logic?

## Slide 13: Elaborate State Machine in text description
Enumerate all possible inputs and outputs
Objective: Insert sufficient coins to release a can of Coke
Either Insert R5 + R5 + R5 in sequence
OR Insert R5 + R10 in sequence
OR Insert R10 + R5 in sequence
OR Insert R10 + R10 in sequence
OR Insert R5 + R5 + R10 in sequence

## Slide 14: Make a State Diagram Representation of State Machine (Moore Machine)
S0
S1
S2
S5
S6
S3
S4
S7
S8
OPEN
OPEN
OPEN
OPEN
OPEN
R5
R10
R5
R10
R5
R10
R5
R10

## Slide 15: Simplifying the State Machine
Identify Similar States (same present state and next state)
State Minimization by Observation
Reset brings to State S0
State S1 represents R5 received so far, one possible path
State S2 represents R10 received so far, two possible paths;
State S3 represents R15 received so far, three possible paths
S4, S5, S6, S7 have identical behaviour so they can be
Combined into one state
S0
S1;
R5
S2;
R10
S3;
R15
OPEN
R10
R5
R10
Reset
R5
R5
R10

## Slide 16: State Transition Table Describing Vending Machine
Q1 | Q0 | Present State | Inputs |  | Next State | Output OPEN
 |  |  | R10 | R5 |  | 
0 | 0 | S0; R0 | 0 | 0 | S0; R0 | 0
 |  |  | 0 | 1 | S1; R5 | 0
 |  |  | 1 | 0 | S2; R10 | 0
 |  |  | 1 | 1 | Not Allowed | X
0 | 1 | S1; R5 | 0 | 0 | S1; R5 | 0
 |  |  | 0 | 1 | S2; R10 | 0
 |  |  | 1 | 0 | S3; R15 | 0
 |  |  | 1 | 1 | Not Allowed | X
1 | 0 | S2; R10 | 0 | 0 | S2; R10 | 0
 |  |  | 0 | 1 | S3; R15 | 0
 |  |  | 1 | 0 | S3; R20 | 0
 |  |  | 1 | 1 | Not Allowed | X
1 | 1 | S3; R15 | 0 | 0 | S3; R15 | 1
 |  |  | 0 | 1 | S3; R15 | 1
 |  |  | 1 | 0 | S3; R15 | 1
 |  |  | 1 | 1 | Not Allowed | X

## Slide 17: State Mapping to Flipflops
In the reduced State Diagram, there are 4 states
We can distinctly represent these states using two Flipflops
Assign states as follows:
States | Code | Q1 | Q0
S0 | 00 | 0 | 0
S1 | 01 | 0 | 1
S2 | 10 | 1 | 0
S3 | 11 | 1 | 1
FF1
FF0
Clk
D1
D0
Q1
Q0
To set
NEW
States
Present
States

## Slide 18: Present State to Next State Table using DFF
Present State |  | Inputs |  | Next State |  | Output OPEN
Q1 | Q0 | R10 | R5 | D1 | D0 | 
0 | 0 (S0) | 0 | 0 | 0 | 0 (S0) | 0
 |  | 0 | 1 | 0 | 1 (S1) | 0
 |  | 1 | 0 | 1 | 0 (S2) | 0
 |  | 1 | 1 | X | X | X
0 | 1 (S1) | 0 | 0 | 0 | 1 (S1) | 0
 |  | 0 | 1 | 1 | 0 (S2) | 0
 |  | 1 | 0 | 1 | 1 (S3) | 0
 |  | 1 | 1 | X | X | X
1 | 0 (S2) | 0 | 0 | 1 | 0 (S2) | 0
 |  | 0 | 1 | 1 | 1 (S3) | 0
 |  | 1 | 0 | 1 | 1 (S3) | 0
 |  | 1 | 1 | X | X | X
1 | 1 (S3) | 0 | 0 | 1 | 1 (S3) | 1
 |  | 0 | 1 | 1 | 1 (S3) | 1
 |  | 1 | 0 | 1 | 1 (S3) | 1
 |  | 1 | 1 | X | X | X

## Slide 19: Characteristic Equation for D0 using K-Map
R10,R5\Q1Q0 | 00 | 01 | 11 | 10
00 | 0 | 1 | 1 | 0
01 | 1 | 0 | 1 | 1
11 | X | X | X | X
10 | 0 | 1 | 1 | 1
R5’.Q0
R5.Q0’
R10.Q1
D0 = (R5’.Q0) + (R5.Q0’) + (R10.Q1) + (Q1.Q0)
Q1Q0

## Slide 20: Present State to Next State Table using DFF
Present State |  | Inputs |  | Next State |  | Output OPEN
Q1 | Q0 | R10 | R5 | D1 | D0 | 
0 | 0 (S0) | 0 | 0 | 0 | 0 (S0) | 0
 |  | 0 | 1 | 0 | 1 (S1) | 0
 |  | 1 | 0 | 1 | 0 (S2) | 0
 |  | 1 | 1 | X | X | X
0 | 1 (S1) | 0 | 0 | 0 | 1 (S1) | 0
 |  | 0 | 1 | 1 | 0 (S2) | 0
 |  | 1 | 0 | 1 | 1 (S3) | 0
 |  | 1 | 1 | X | X | X
1 | 0 (S2) | 0 | 0 | 1 | 0 (S2) | 0
 |  | 0 | 1 | 1 | 1 (S3) | 0
 |  | 1 | 0 | 1 | 1 (S3) | 0
 |  | 1 | 1 | X | X | X
1 | 1 (S3) | 0 | 0 | 1 | 1 (S3) | 1
 |  | 0 | 1 | 1 | 1 (S3) | 1
 |  | 1 | 0 | 1 | 1 (S3) | 1
 |  | 1 | 1 | X | X | X

## Slide 21: Characteristic Equation for D1 using K-Map
R10,R5\Q1Q0 | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 1
01 | 0 | 1 | 1 | 1
11 | X | X | X | X
10 | 1 | 1 | 1 | 1
Q1
R10
R5.Q0
D1 = Q1 + R10 + (R5.Q0)

## Slide 22: Present State to Next State Table using DFF
Present State |  | Inputs |  | Next State |  | Output OPEN
Q1 | Q0 | R10 | R5 | D1 | D0 | 
0 | 0 (S0) | 0 | 0 | 0 | 0 (S0) | 0
 |  | 0 | 1 | 0 | 1 (S1) | 0
 |  | 1 | 0 | 1 | 0 (S2) | 0
 |  | 1 | 1 | X | X | X
0 | 1 (S1) | 0 | 0 | 0 | 1 (S1) | 0
 |  | 0 | 1 | 1 | 0 (S2) | 0
 |  | 1 | 0 | 1 | 1 (S3) | 0
 |  | 1 | 1 | X | X | X
1 | 0 (S2) | 0 | 0 | 1 | 0 (S2) | 0
 |  | 0 | 1 | 1 | 1 (S3) | 0
 |  | 1 | 0 | 1 | 1 (S3) | 0
 |  | 1 | 1 | X | X | X
1 | 1 (S3) | 0 | 0 | 1 | 1 (S3) | 1
 |  | 0 | 1 | 1 | 1 (S3) | 1
 |  | 1 | 0 | 1 | 1 (S3) | 1
 |  | 1 | 1 | X | X | X

## Slide 23: Characteristic Equation for OPEN using K-Map
R10,R5\Q1Q0 | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 0
01 | 0 | 0 | 1 | 0
11 | X | X | X | X
10 | 0 | 0 | 1 | 0
Q1Q0
OPEN = Q1Q0

## Slide 24: Vending Machine Circuit using DFF
DFF
0
DFF
1
D0
Q0
Q0’
Q1
Q1’
D1
Clk
R5’
Q0
R5
Q0’
R10
Q1
R5
Q0
R10
Q1
OPEN
Coin Detector
R5
R10
Q1
Q0

## Slide 25: Moore State Machine for Vending Machine
S0
[0]
S1
[0]
S2;
[0]
S3;
[1]
OPEN
R10
R5
R10
Reset
R5
R5+R10
(R5’R10’+Reset)
R5’R10’
Reset’
Reset
R5’R10’

## Slide 26: Mealy State Machine for Vending Machine
S0
S1
S2
S3
OPEN
R10/0
R5/0
R10/1
Reset
R5/0
R5+R10/1
(R5’R10’+Reset)/0
R5’R10’/0
Reset’/1
Reset/0
R5’R10’/0

## Slide 27: Some Comparison Moore vs Mealy
Mealy machine requires fewer states to reach output in comparison with Moore machine
Mealy machine is more susceptible to glitches
Explicit output values are shown in Mealy machine associated with each transition
Output changes after state is changed in Moore machine
Output in Moore machine depends upon state only; inputs can steer the output towards a particular state that affects output
Output depends upon present state and the present value at the input; thus, output can change immediately with the change in input, independent of synchronous clock.

## Slide 28: One Hot Encoding – one FF for each state
Present State |  |  |  | Inputs |  | Next State |  |  |  | Output OPEN
Q3 | Q2 | Q1 | Q0 | R10 | R5 | D3 | D2 | D1 | D0 | Y
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 
 |  |  |  | 0 | 1 | 0 | 0 | 1 | 0 | 
 |  |  |  | 1 | 0 | 0 | 1 | 0 | 0 | 
 |  |  |  | 1 | 1 | X | X | X | X | 
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 
 |  |  |  | 0 | 1 | 0 | 1 | 0 | 0 | 
 |  |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 1
 |  |  |  | 1 | 1 | X | X | X | X | 
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 
 |  |  |  | 0 | 1 | 1 | 0 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 1
 |  |  |  | 1 | 1 | X | X | X | X | 
1 | 0 | 0 | 0 | X | X | 1 | 0 | 0 | 0 | 1
The Design Becomes Simpler
Less Combinational Logic – At the Expense of Extra DFF
D3 is directly
the Output and
Its State

## Slide 29: Algorithmic State Machine Description - ASMD
State Box
List Outputs
xyz
State Name
Condition
Output
Box
Exit to Other
ASM Blocks
True
False
State Code
Exit to Other
ASM Blocks

## Slide 30: Topics
(Leftover) Example of Vending Machine
State Minimization
Row Matching Method
Using Implication Charts
QUIZ 2 today

## Slide 31: Moore State Machine for Vending Machine
S0
[0]
S1
[0]
S2;
[0]
S3;
[1]
OPEN
R10
R5
R10
Reset
R5
R5+R10
(R5’R10’+Reset)
R5’R10’
Reset’
Reset
R5’R10’

## Slide 32: Mealy State Machine for Vending Machine
S0
S1
S2
S3
OPEN
R10/0
R5/0
R10/1
Reset
R5/0
R5+R10/1
(R5’R10’+Reset)/0
R5’R10’/0
Reset’/1
Reset/0
R5’R10’/0

## Slide 33: Some Comparison Moore vs Mealy
Mealy machine requires fewer states to reach output in comparison with Moore machine
Mealy machine is more susceptible to glitches
Explicit output values are shown in Mealy machine associated with each transition
Output changes after state is changed in Moore machine
Output in Moore machine depends upon state only; inputs can steer the output towards a particular state that affects output
Output depends upon present state and the present value at the input; thus, output can change immediately with the change in input, independent of synchronous clock.

## Slide 34: One Hot Encoding – one FF for each state
Present State |  |  |  | Inputs |  | Next State |  |  |  | Output OPEN
Q3 | Q2 | Q1 | Q0 | R10 | R5 | D3 | D2 | D1 | D0 | Y
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 
 |  |  |  | 0 | 1 | 0 | 0 | 1 | 0 | 
 |  |  |  | 1 | 0 | 0 | 1 | 0 | 0 | 
 |  |  |  | 1 | 1 | X | X | X | X | 
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 
 |  |  |  | 0 | 1 | 0 | 1 | 0 | 0 | 
 |  |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 1
 |  |  |  | 1 | 1 | X | X | X | X | 
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 
 |  |  |  | 0 | 1 | 1 | 0 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 1
 |  |  |  | 1 | 1 | X | X | X | X | 
1 | 0 | 0 | 0 | X | X | 1 | 0 | 0 | 0 | 1
The Design Becomes Simpler
Less Combinational Logic – At the Expense of Extra DFF
D3 is directly
the Output and
Its State

## Slide 35: Algorithmic State Machine Description - ASMD
State Box
List Outputs
xyz
State Name
Condition
Output
Box
Exit to Other
ASM Blocks
True
False
State Code
Exit to Other
ASM Blocks